## Slide 1: Enterprise Wi-Fi Worms, Backdoors and Botnets for Fun and Profit
Vivek Ramachandran
Founder, SecurityTube.net

## Slide 2: Vivek Ramachandran
WEP Cloaking
Defcon 15
Caffe Latte Attack
Toorcon 9
Microsoft
Security Shootout
Wi-Fi Malware, 2011
802.1x, Cat65k
Cisco Systems
B.Tech, ECE
IIT Guwahati
Media Coverage
CBS5, BBC
Trainer, 2011

## Slide 3: In-Person Trainings

## Slide 4: SecurityTube Online Certifications
25+ Countries

## Slide 5: Free DVD (12+ Hours of HD Videos)
http://www.securitytube.net/downloads

## Slide 6: Enterprise Wi-Fi Worms, Backdoors and Botnets for Fun and Profit
Vivek Ramachandran
Founder, SecurityTube.net

## Slide 7: Objective
How Malware could leverage Wi-Fi to create
  Backdoors
  Worms
  Botnets

## Slide 8: Background – Understanding Wi-Fi Client Software
Allows Client to connect to an Access Point
First time user approves it, Auto-Connect for future instances
Details are stored in Configuration Files

## Slide 9: Command Line Interaction?
Scanning the air for stored profiles
Profiling the clients based on searches
Different clients behave differently
Demo

## Slide 10: See All Wi-Fi Interfaces
Netsh wlan show interfaces

## Slide 11: Drivers and Capabilities
Netsh wlan show drivers

## Slide 12: Scan for Available Networks
Netsh wlan show networks

## Slide 13: View Existing Profiles
Netsh wlan show profiles

## Slide 14: Starting a Profile
Netsh wlan connect name=“vivek”

## Slide 15: Export a Profile
Netsh wlan export profile name=“vivek”

## Slide 16: Creating an Access Point on a Client Device
Requirement for special drivers and supported cards
Custom software used – HostAPd, Airbase-NG
More feasible on Linux based systems

## Slide 17: Generation 2.0 of Client Software – Hosted Network
Available Windows 7 and Server 2008 R2 onwards
Virtual adapters on the same physical adapter
SoftAP can be created using virtual adapters
  DHCP server included
“With this feature, a Windows computer can use a single physical wireless adapter to connect as a client to a hardware access point (AP), while at the same time acting as a software AP allowing other wireless-capable devices to connect to it.”
http://msdn.microsoft.com/en-us/library/dd815243%28v=vs.85%29.aspx

## Slide 18: Feature Objective
To allow creation of a wireless Personal Area Network (PAN)
  Share data with devices
Network connection sharing (ICS) with other devices on the network

## Slide 19: Demonstration
Demo of Hosted Network

## Slide 20: Creating a Hosted Network

## Slide 21: Driver Support

## Slide 22: Client still remains connected to hard AP!

## Slide 23: Wi-Fi Backdoor
Easy for malware to create a backdoor
They key could be:
  Fixed
  Derived based on MAC address of host, time of day etc.
As host remains connected to authorized network, user does not notice a break in connection
No Message or Prompt displayed

## Slide 24: Understanding Rogue Access Points
Rogue AP

## Slide 25: Makes a Rogue AP on every Client!
Rogue AP
Rogue AP
Rogue AP

## Slide 26: Best Part – No Extra Hardware!

## Slide 27: Advantages?
Internet

## Slide 28: Advantages?
Internet
Wicked Network

## Slide 29: Why is this cool?
Victim will never notice anything unusual unless he visits his network settings
  has to be decently technical to understand
Attacker connects to victim over a private network
  no wired side network logs: firewalls, IDS, IPS
  Difficult, if not impossible to trace back
  Difficult to detect even while attack is ongoing 
Abusing legitimate feature, not picked up by AVs, Anti-Malware
More Stealth? Monitor air for other networks, when a specific network comes up, then start the Backdoor

## Slide 30: Chaining Hosted Networks like a proxy?
Each node has client and AP capability
We can chain them to “hop” machines
Final machine can provide Internet access
Like Wi-Fi Repeaters

## Slide 31: Chaining Infected Laptops
AP
AP
AP
Client
Client
Client
Authorized
AP

## Slide 32: Package Meterpreter for full access?
Once attacker connects to his victim, he would want to have access to everything
Why not package a Meterpreter with this? 
How about a Backdoor post-exploitation script for Metasploit? 

## Slide 33: Demo
Coupling Hosted Network with Metasploit

## Slide 34: Increasing Stealth
Passive Monitoring for SSIDs available
Trigger SSID causes Wicked Hosted Network to start and create application level backdoor
Attacker connects and does his job
Shuts off Trigger SSID and Malware goes to Passive Monitoring again

## Slide 35: Karmetasploit
Victim connects by mistake or misassociation
Victim opens browser, Metasploit Browser_Autopwn exploits the system
Hacker gets access!
Biggest Challenge – Victim notices he is connected to the wrong network and disconnects himself

## Slide 36: Enhancing Karmetasploit
Upon Exploitation, create the hosted network backdoor
User disconnects, but this hosted network still remains active
Attacker connects via this network

## Slide 37: What about older clients and other OSs?
Windows < 7, Mac OS do not have the Hosted Network or alike feature
  Use Ad-Hoc networks
  Use Connect Back mechanism 
    When a particular SSID is seen, connect to it automatically
    Blurb reporting “Connected to ABC”
      Could we kill it? 

## Slide 38: Hosted Network Meterpreter Scripts
http://zitstif.no-ip.org/meterpreter/rogueap.txt
http://www.digininja.org/projects.php

## Slide 39: Dissecting Worm Functionality
Exploit
Worm
Propagation
Technique

## Slide 40: Hosted Network Encryption
Uses WPA2-PSK for encryption
Key is encrypted in configuration file
Can be decrypted 
What if there is an office network configured on the same machine with WPA2-PSK?

## Slide 41: 1. Infect Authorized Computer and Decrypt Passphrase

## Slide 42: Decryption Routine

## Slide 43: Alternate – Dump and Copy

## Slide 44: 2. Create a Soft Access Point with the same Credentials
OfficeAP
OfficeAP
Worm Infected Laptop

## Slide 45: 3. Signal Strength Game
OfficeAP
OfficeAP
Worm Infected Laptop

## Slide 46: 4. Hop and Exploit
OfficeAP
Exploit

## Slide 47: 5. Replicate and Spread
OfficeAP
OfficeAP

## Slide 48: Worms Wi-Fi Network Signal Strength > AP
OfficeAP
OfficeAP
OfficeAP
OfficeAP
OfficeAP

## Slide 49: Wi-Fi Worm
Retrieve the network key for the network
Create a hosted network with the same name
When the victim is in the vicinity of his office, worm can be activated
At some point the signal strength may be higher than real AP
Other colleagues laptops may hop and connect
  Conference rooms, Coffee and Break areas

## Slide 50: Why is this interesting?
Worm uses its own private Wi-Fi network to propagate
Does not use the Wired LAN at all
Difficult for network defenses to detect and mitigate 
Targeted APT against an Enterprise

## Slide 51: Demo

## Slide 52: On the Run 

## Slide 53: APIs for the Hosted Network Feature

## Slide 54: Questions
Questions?

## Slide 55: Enterprise Wi-Fi Worms, Backdoors and Botnets for Fun and Profit
Thank You!